## Slide 1: Knots every pirate needs
Four knots, from the easiest to the most useful.
Notes: Ask the crew which knot they already know before starting.

## Slide 2: Bowline
Makes a fixed loop at the end of a line that won't slip.
Notes: The rabbit comes out of the hole, round the tree and back down the hole. Pirates call it the king of knots.

## Slide 3: Clove hitch
Ties a line to a post quickly; easy to adjust.
Notes: It can slip under a changing load: back it up with two half hitches.

## Slide 4: Reef knot
Joins two ends of the same line, for reefing sails.
Notes: Right over left, then left over right. Never use it to join two different ropes.

## Slide 5: Figure eight
A stopper knot at the end of a line.
Notes: Tie it at the end of every sheet so it can't run out of the block.